## Slide 1: Krafthack 2022
Runner bolts tensional load prediction
Team: Sopra Steria Team 2

## Slide 2: Initial Thoughts
Started thinking about data augmentation.
  Lack of features in test-dataset.
How to highlight and learn temporal features from dataset.

## Slide 3: Data processing
Removed all vibration data.
Removed all rows containing nan values.
Translated mode values to 0 and 1’s.
Translated original timestamp to two features.
  Day of week and hour of day.
Scaling training and test data, zero mean and 1 std.
  Scikit Learn Standardcaler fitted to training data.

## Slide 4: Feature engineering
Augment dataset with data calculable from test-dataset.
Added feature representing current operation duration in seconds.
  Bolt tensile tention could potensially rise or decline after turbine startup.
Sliding window feature addition.
Adding previous output as a feature for the next prediction.

## Slide 5: Training and validation split
Training dataset split into training and validation data.
  70% training data, 30% validation data.
Training and validation data not split randomly.

## Slide 6: Models and results
Linear Regression, all default values (SkLearn)
XGBoost, XGBRegressor (booster=gbtree, learning_rate=0.2, gamma=0.1, max_depth=6, eval_metric=‘mae’)
Catboost, CatBoostRegressor (iterations=400)

## Slide 7: Linear Regression
Simple baseline model
Drawback:
  Highly correlated data from data preprocessing
  Might lead to overfitting

## Slide 8: Results

## Slide 9: Discussion
Suggestion for future hackathon:
  Use anomaly detection to find optimal guide vane opening for a single turbine/generator regarding tension and torsion in the bolts.
  This might expose guide vane value ranges causing higher stress.
  Optimize the guide vane openings of all turbines to run at a non-harmful guide vane value, while providing the required reactive power.